| Existing & Proposed Desalination Plants in California. Status Update August 2008 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Operator | Location | Co-located? | Max Capacity MGD | Max Capacity (m3/d) | Intake | Discharge | Status | Acre feet per day | Acre feet per year | GHG in pounds of CO2 equivalance at 780 lb/KWh (assumes 4.4 KWh/acre ft) | Tons of CO2 |
| Marin Municipal Water District | San Rafael | No | 15 | 38,000 to 57,000 | Surface | Mixed with WW | pilot plant completed; Engineering report on pilot plant released in '06; cost estimate $2000-$3000/AF; EIR due out in Spring 2007 | 46 | 16,790 | 57,623,280.0 | 26,133.0 |
| EBMUD/SFPUC/Contra Costa Water District/Santa Clara Valley Water District | Pittsburg/ Oakland/ Oceanside | Likely | 50 | 450,000 | Surface | Not known | planning to build pilot plant at Contra Costa Mallard Slough pumping plant; in contracting phase; pilot test will run through 2008 and into 2009 | 153 | 56,000 | 192,192,000.0 | 87,162.0 |
| East Bay MUD | Crockett | No | 2 | 7,600 | Surface | N/A | received Prop.50 funding to build the plant; internal discussion about implementation scheduling; no plans for pilot test but may do bench scale testing | 6.1 | 2,241 | 7,691,112.0 | 3,488.0 |
| Montara Water and Sanitary District | Montara | No | N/A | N/A | N/A | N/A | conducting feasibility study; draft sometime this summer |  |  |
| City of Santa Cruz | Santa Cruz | No | 3 | 9,500, possible expansion to 17,000 | Surface | Mixed with WW | pilot plant to begin in summer '07 and continue for 12 months; technical review/design in 2008; EIR in 2009; if approved, construction in 2010-2011 | 9.2 | 3,361 | 11,534,952.0 | 5,231.3 |
| California American Water Company | Moss Landing | Yes | 12 | 42,000 to 45,000 | Surface | Surface | EIR expected this summer; received permits for pilot plant; desal response group sued but didn't get injunction to stop the pilot plant; got permits from Central Coast Regional Water Quality Control Board | 36.8 | 13,443 | 46,136,376.0 | 20,923.5 |
| Pajaro-Sunny Mesa/Poseidon | Moss Landing | Yes | 25 | 76,000 to 95,000 | Surface | Surface | Completed pilot plant? Next step would be to prepare EIR | 76.7 | 28,003 | 123,213.2 | 55.9 |
| City of Sand City | Sand City | No | 0.3 | 1,100 | Subsurface | Subsurface | Received Prop. 50 for construction; have Coastal Development Permit but will need to get extension; enginner working w/State Water Resources Control Board and awaiting permit from DHS | 0.9 | 336 | 1,153,152.0 | 523.0 |
| Monterey Peninsula Water Management District | Sand City | No | 8 | 30,000 | Subsurface | Subsurface | still on-hold; put on-hold b/c wasn't large enough to meet SWRCB Order 95-10 | 24.6 | 8,961 | 30,754,152.0 | 13,947.5 |
| Marina Coast Water District | Marina | No | 1.5 |  | Subsurface | Subsurface | have pilot plant that was constructed a while back, but don't plan on firing it up; completed pre-design report; do not need water right away and thus is sitting back to see if a regional plant with Cal-Am makes more sense | 4.6 | 1,679 | 5,762,328.0 | 2,613.3 |
| Ocean View Plaza | Cannery Row | No | 0.05 | 190 | Surface | Surface | submitted coastal permit application to Coastal Commission in 12/2006; have not been put on an agenda yet | 0.15 | 55 | 188,760.0 | 85.6 |
| Cambria Community Services District/Department of the Army | Cambria | No | 0.5 | 1,900 | Subsurface | Subsurface | Coastal Commission delayed ruled on whether District can conduct geotechnical investigations b/c may require an amendment to the local coastal plan; investigation of the beach will continue after CC reconvenes and the snowy plover nesting season is over | 1.5 | 558 | 1,915,056.0 | 8,684.8 |
| Arroyo Grande/Grover Beach/Oceano Community Services District | Oceano | No | 2 | 7,600 | Subsurface | Mixed with WW | conducting feasibility studies | 6.1 | 2,241 | 7,691,112.0 | 3,488.0 |
| Los Angeles Deptartment of Water and Power | Playa Del Rey | Yes | 25 | 45,000 to 95,000 | Surface | Mixed w/cooling water or WW | completed fatal flaw analysis; trying to get approval from Board for a pilot plant; hoping to go to Board in a month or two | 76.7 | 28,003 | 96,106,296.0 | 43,585.6 |
| West Basin Municipal Water District | El Segundo | Yes | 20 | 76,000 | Surface | Surface | pilot plant running since 5/02; will run into 2008 or 2009; working on demonstration project at Redondo Beach of 0.5 MGD intake capacity; will look at wedge wire screen for open intake and subsurface intake; permitting process for demonstration plant will probably take 18 months; hope to have demo.plant running by 2010; run for few years | 61.4 | 22,404 | 76,890,528.0 | 34,871.0 |
| Long Beach Water Department | Long Beach | No | 9 | 34,000 | Subsurface | Subsurface | prototype plant is operational; began 2007 and will run through 2010; capacity is 300,000 gallons per day and is primarily looking at the membrane element using water from Haynes Generating Station (they do not plan to co-locate the final desal plant); they will also conduct assessments on intakes at a site that will more closely resemble the project site | 27.6 | 10,081 | 34,597,992.0 | 15,690.7 |
| Poseidon Resources | Huntington Beach | Yes | 50 | 190,000 | Surface | Surface | EIR certified; challenged by Desal Response Group, which lost in court (Desal Response Group is now challenging all of the permits that they have received thus far b/c the OTC system will be removed, constituting a major change to the project); Poseidon is still waiting to hear about Coastal Development Permit from Coastal Commission | 153.4 | 56,000 | 192,192,000.0 | 87,161.9 |
| Municipal Water District of Orange County | Dana Point | No | 15 | 57,000 | Subsurface | Mixed with WW | completed feasibility study in March 2007; demonstration project completed May 2006; | 46 | 16,801 | 57,661,032.0 | 26,150.1 |
| Poseidon Resources | Carlsbad | Yes | 50 | 190,000, possible expan-sion to 300,000 | Surface | Surface | awaiting Coastal Development Permit from the Coastal Commission; hearing scheduled for November 15, 2007 | 153.4 | 56,000 | 192,192,000.0 | 87,161.9 |
| PG&E Diablo Canyon Power Plant |  | 0.6 | 2,180 |  |  | Active | 1.8 | 672 | 2,306,304.0 | 1,045.9 |
| Duke Energy, Morro Bay Power Plant |  | 0.4 | 1,630 |  |  | Not known | 1.2 | 449 | 1,540,968.0 | 698.9 |
| Duke Energy, Moss Landing Power Plant |  | 0.5 | 1,820 |  |  | Active | 1.5 | 558 | 1,915,056.0 | 868.5 |
| U.S. Navy, San Nicolas Island |  |  | 0.07 |  |  |  | Not known | 0.2 | 76.7 | 263,234.4 | 119.4 |
| Chevron/Gaviota |  |  | 0.4 | 1,550 |  |  | Active | 1.2 | 449 | 1,540,968.0 | 698.9 |
| City of Morro Bay |  |  | 0.6 | 2,270 |  |  | Intermittent use | 1.8 | 672 | 2,306,304.0 | 1,045.9 |
| Marina Coast Water District |  |  | 0.3 | 1,140 |  |  | Temporarily idle | 0.9 | 336 | 1,153,152.0 | 523.0 |
| Monterey Bay Aquarium |  |  | 0.04 | 150 |  |  | Active | 0.1 | 44 | 151,008.0 | 68.5 |
| Santa Catalina Island |  |  | 0.1 | 500 |  |  | Inactive | 0.3 | 113 | 387,816.0 | 175.9 |
| Total |  |  | 290 |  |  |  |  | 893.15 | 326,327 | 1,023,970,151.6 | 472,202.0 |

# Text boxes

EXHIBIT D

EXISTING & PROPOSED DESALINATION PLANTS